## Slide 1: Wheel Assembly Layout Proposal
Project Velocity: Aurora Express

## Slide 2
Work Area
Crane

## Slide 3: Bottleneck analysis
The goal of this analysis is to identify bottlenecks and suggest ways to improve and enhance the wheel assembly of the Aurora Express. The study involves time study based on the data provided.
The time study provided includes observed time, average, range, description and notes of various processes involved in the wheel assembly process.
According to the study, the maximum time taken is in the process of Mounting wheel to axle, which is because it involves heaviest component that requires crane and the timing varies by equipment availability, the average time taken for this process is 05:21 .
Secondly it takes upto 04:44 on average to conduct the wheel alignment which requires specialized equipment and precision is the key. Thirdly, it takes upto 04:16 to assemble hub to wheel frame because it requires manual dexterity and precision .
Fourth comes bleed to brake system which takes 04:07 in average this is because of variation in the techniques.
Lastly it takes 04:01 average time to fit brakes to disc which involves heavy lifting and precise alignment.
According to the study the process in which more variation in time was noticed are to assemble hub to wheel frame(00:28), lubricating wheel bearings(00:29), secure wheel with locking(00:30), perform functionality test with wheel assembly (0:28) and transporting assembly to next section(00:30).

## Slide 4: Recommendations
The suggestive ways to improve efficiency for the most common processes which have variations as well as more time taking such as bleeding brake system which varies because of the variation in techniques , to solve this problem the operators involved in this process must learn techniques and be trained , this way this process could take less time.
Another recommendation would be that since mounting wheel to axle varies with equipment availability ensuring the equipment and tools must be available and ready soon to ensure smooth ongoing and less wastage of time .
Third to assemble hub to wheel it requires manual dexterity and precisions so training must be given to the operators with techniques to reduce the bottle necks. In conclusion, by focussing on the processes such as bleed brake system and mounting wheel to axle by making equipment available with the tools and cranes and operators training on standardized techniques could make the bottlenecks reduce and help streamline processes and meet production goals efficiently.

## Slide 5: Original Layout
WHEEL
PRESS
ASSEMBLY 1
WAREHOUSE
ASSEMBLY 3
ASSEMBLY 4
Crane
ASSEMBLY 2
61:15
62:35
62:25
61:47
62:10
62:43
61:46
62:52

## Slide 6: Original Layout pinpoints
In the original layout, there is only one crane that moves from left to right to lift and transport heavy components, which creates several inefficiencies in the workflow. The crane’s movement across the entire assembly line results in delays, as it can only serve one area at a time. As a result, Assembly 1 and Assembly 3 receive components earlier than Assembly 2 and Assembly 4, leading to idle time in these later stations. This imbalance in component delivery not only wastes time but also reduces the overall productivity of the assembly line, as stations remain idle while waiting for parts.
Furthermore, the distance between the wheel press and the warehouse is significant, causing the crane to travel long distances to deliver components to the warehouse. This long transport route not only slows down the material flow but also consumes unnecessary time, contributing to a delay in the overall process. As the crane moves from one end of the line to the other, the time spent on these long journeys reduces the efficiency of material handling, which could otherwise be optimized.
Additionally, there is extra space in the current layout that remains underutilized, especially near the wheel press and between assembly stations. This unutilized space exacerbates the crane's inefficiency by increasing the travel distance to the final destination, i.e., the warehouse. The crane spends excessive time reaching the warehouse due to the poorly optimized layout, ultimately wasting both time and space.
These inefficiencies in the current setup could be addressed by reconfiguring the layout to reduce travel distances, ensure a balanced flow of components to all assembly stations, and better utilize available space, which would significantly improve overall efficiency and productivity.

## Slide 7: New Layout
WHEEL
PRESS
ASSEMBLY 1
WAREHOUSE
ASSEMBLY 3
ASSEMBLY 4
Crane
ASSEMBLY 2

## Slide 8: New Layout summary
In the proposed layout, the addition of two cranes plays a crucial role in reducing wait times and improving overall efficiency. With one crane positioned on each side of the central wheel press, both cranes can operate simultaneously, lifting and transporting components to the four assembly stations without delay. This setup minimizes bottlenecks that typically occur when only one crane is available, ensuring that heavy parts are moved quickly and without unnecessary waiting.
By relocating the wheel press to the center of the four assembly areas, it shortens the distance for transporting components between stations, resulting in a faster and more efficient material flow. This central position allows the cranes to access the wheel press from either side, further speeding up the delivery process and reducing transport time between workstations.
Additionally, this layout optimizes space utilization by positioning equipment and workstations in a way that maximizes accessibility and minimizes congestion. The flow of materials becomes more streamlined, and workers can operate with fewer obstacles, improving both productivity and workspace efficiency.
Overall, this new configuration not only saves time by reducing transport delays but also creates a more organized, compact, and efficient workspace, allowing for better utilization of space and a smoother assembly process.